# Emissions Readiness Check and Drive Cycle Procedures

I was having a hard time finding the specifics of how to get all the emission checks to a ready state after clearing a CEL or resetting the battery. My friend had a NCVECS OBD II Drive Traces CD which shows specifically how to ensure everything is in the ready state:
=========
EGR Monitor:
=========
Preq:
MIL must be off
Altitude is below 7801 feet
IAT (Intake Air Temperature) must be above 13F
Driving Procedure:
1) Connect scan tool in order to observe data stream and monitor status.
2) If IAT is less than 50F at engine start-up, idle engine for 10 minutes.
3) Drive the vehicle at a steady speed between 43 & 56 mph for three to five minutes. (Do not exceed 30% TPS; maintain smooth throttle inputs and avoid sudden accelerations)
=================
O2 Sensor Heater Monitor
=================
Preq:
MIL must be off
Drive Procedure:
1) Start engine and allow it to idle for 9 minutes
2) Drive the vehicle at 25 mph or more for at least 2 minutes.
==============
Evaporative Monitors
==============
Preq:
MIL must be off
Fuel level is between 1/2 and 3/4 full
Altitude is below 7801 feet
Engine Coolant Temperature (ECT) & IAT is between 40-95 F
Cold Soak Procedure:
*1) Start the engine and allow ECT to reach 176F or higher, either by idling or driving
*2) Let the vechile sit for 8 hours, or until the difference between IAT and ECT is less than 13F
Driving Procedure:
1) Connect scan tool in order to observe data stream and monitor status.
2) Release pressure in the fuel tank by removing and re-installing fuel cap before start-up
3) Smoothly drive the vehicle for 15 minutes at 45 mph
4) Check monitor status
5) If monitor has not set, smoothly drive the vehicle for 15 minutes at 25 mph
*Include two stops of 30 seconds during the 15 minute period
==============
Catalyst Monitor
==============
Preq:
MIL must be off
ECT must be 176F or more
IAT must be 14F or more
Driving Procedure:
1) Connect scan tool in order to observe data stream and monitor status.
2) Note the IAT data for use in step 3
3) Drive the vehicle at a steady speed between 40-55 mph or more for:
3a) 7 minutes if IAT was below 50F at start-up
3b) 3 minutes if IAT was above 50F at start-up
4) Drive the vehicle at 35-45 mph for 7 minutes
==============
o2 Sensor Monitors
==============
Preq:
MIL must be off
Driving Procedure:
1) Connect scan tool in order to observe data stream and monitor status.
2) Start the engine and allow it to idle for at least 2 minutes.
3) Drive the vehicle at 25 mph or more for at least 50 seconds; maintain engine speed above 900 rpm
4) Stop the vehicle and idle the engine for at least 40 seconds
5) Repeat steps 3 & 4 until monitor sets or a maximum of 10 times
***I compiled the list below based on everything set above for a full drive cycle readiness checklist:
==============
Full Driving Procedure
==============
Preq:
MIL must me off
Fuel at 1/2 to 3/4 full
Allow engine coolant temp to warm up to 176F (Drive home from work/etc.)
Let car sit for 8 hours+
Driving Procedure:
(When driving, do not exceed 30% TPS and maintain smooth throttle input while avioding sudden acceleration)
Remove fuel cap and reinstall
Start Engine
Idle for 10 minutes
Drive for ~45mph for 15 minutes with two stops of 30 seconds
Repeat the following until all systems are ready (max 10 times):
Drive for >25mph for 1 minute
Stop vehicle and idle for 1 minute
Thanks,
HK

Source: https://www.my.is/threads/emissions-readiness-check-and-drive-cycle-procedures.428910/